Superboard II Quick Reference
For the Briel Computers Superboard ///
Jeff Tranter <tranter@pobox.com>
29-Jan-2015

General Specifications
CPU	65C02
Clock Speed	1 MHz
RAM	32 KB
ROM	10 KB
Keyboard	Integral 53-key
Video	Composite
Power Input	USB 5V host or power supply 1000mA or more
Serial Port Settings	9600 bps 8N1, no handshaking, no flow control

Memory Map

Address Range	Comments
$0000 - $00FF	Zero page RAM.
$0100 - $01FF	Stack RAM.
$0000 - $7FFF	RAM (32K Superboard ///).
$A000 - $BFFF	ROM (BASIC).
$D085 - $D39D	Video memory (25x25 mode).
$D080 - $D3FF	Video memory (32x28 mode).
$DF00	Keyboard (write row, read column). Decimal 57088.
$F000	6850 ACIA status/control register. Decimal 61440.
$F001	6850 ACIA data register. Decimal 61441.
$F800-$FFFF	ROM (OSI routines and monitor).

ROM Monitor Commands

Display: AAAA DD

In address mode, enter 4 character hex address. In data mode, enter 2 character hex data.

"/" enters data mode.
"." enters address mode.
<Return> (in data mode) advances to next address.
"L" (in address mode) loads from cassette tape/serial port.
"G" (in address mode) starts execution from current address mode.

Useful Routines

Address	Description
$0006,$0007	Address to call get argument of USR() function. Value is returned in $00AE,F.
$000D	Number of NULLs to send as per BASIC NULL command.
$000F	BASIC terminal width.
$0064	BASIC <Control>O flag.
$00FB	ROM monitor load flag(non-zero=load mode).
$00FC	ROM monitor contents of current address.
$00FE,$00FF	ROM monitor current address.
$0100	NMI address.
$01C0	IRQ address.
$0200	Cursor position for BASIC output is $D300 +($0200). Default (bottom left) is $65.
$0203	LOAD flag ($80=load from tape).
$0205	SAVE flag (0=not in save mode).
$0212	BASIC <Control>C flag (non-zero=ignore <Control>C). Reset by RUN.
$023E,$023F	Address of BASIC USR() function.
$A274	BASIC warm start.
$BD11	BASIC cold start.
$BF2D	Send character in A to terminal screen. Handles CR, LF, etc.
$FCB1	Send character in A to ACIA.
$FD00	Get key from keyboard and return in A.
$FE00	ROM monitor entry point.
$FE80	Get character from ACIA and return in A.
$FF00	Reset address.
$FFFA,$FFFC	NMI vector.
$FFFC,$FFFD	Reset vector.
$FFFE,$FFFF	IRQ vector.

Microsoft BASIC

Commands: CONT, LIST, NEW, NULL, RUN

Statements: CLEAR, DATA, DEF, DIM, END, FN, FOR, GOSUB, GOTO, IF, INPUT, LET, LOAD, NEXT, NOT, NULL, ON, OR, POKE, PRINT, READ, REM, RESTORE, RETURN, SAVE, STEP, STOP, THEN, TO, WAIT, ?

Functions: ABS(), ASC(), ATN(), CHR$(), COS(), EXP(), FRE(), INT(), LEFT$(), LEN(), LOG(), MID$(), PEEK(), POS(), RIGHT$(), RND(), SGN(), SIN(), SPC(), SQR(), STR$(), TAB(), TAN(), USR(), VAL()

Operators: +, -, *, /, ^, NOT, AND, OR, =, <, >, <>, >=, <=

Editing:

<Shift>+O	Erase last character	<Shift>+P	Erase current line
<Control>+C	Interrupt running program or LIST command.	<Control>+O	Suspend output until ano
Boot prompt:

D/C/W/M ?_
 | | | |
 | | | +--> ROM Monitor
 | | +-----> Warm start (does not clear any BASIC program)
 | +---------> Cold start (clears any BASIC program)
+------------> Disk boot (requires disk controller)

Default video is 25 chars x 25 lines. Power on with BREAK key down to get 32 chars x 28 lines.

Serial Port protocol: 9600 bps, 8N1, no flow control or hardware handshaking. For BASIC, use 50ms char delay, 200ms line delay.