Superboard II Quick Reference
For the Briel Computers Superboard ///
Jeff Tranter <tranter@pobox.com>

General Specifications
CPU	65C02
Clock Speed	1 MHz
RAM	32 KB
ROM	10 KB
Keyboard	Integral 53-key
Video	Composite
Power Input	USB 5V host or power supply 1000mA or more
Serial Port Settings	9600 bps 8N1, no handshaking, no flow control

Memory Map

Address Range	Comments
$0000 - $00FF	Zero page RAM.
$0100 - $01FF	Stack RAM.
$0000 - $7FFF	RAM (32K Superboard ///).
$A000 - $BFFF	ROM (BASIC).
$D085 - $D39D	Video memory (25x25 mode).
$D080 - $D3FF	Video memory (32x28 mode).
$DF00	Keyboard (write row, read column). Decimal 57088.
$F000	6850 ACIA status/control register. Decimal 61440.
$F001	6850 ACIA data register. Decimal 61441.
$F800-$FFFF	ROM (OSI routines and monitor).

ROM Monitor Commands

Display: AAAA DD

In address mode, enter 4 character hex address. In data mode, enter 2 character hex data.

"/" enters data mode.
"." enters address mode.
<Return> (in data mode) advances to next address.
"L" (in address mode) loads from cassette tape/serial port.
"G" (in address mode) starts execution from current address mode.

Useful Routines

Address	Description
$000B,$000C	Address to call get argument of USR() function. Value is returned in $00AE,F.
$000D	Number of NULLs to send as per BASIC NULL command.
$000F	BASIC terminal width.
$0064	BASIC <Control>O flag.
$00FB	ROM monitor load flag(non-zero=load mode).
$00FC	ROM monitor contents of current address.
$00FE,$00FF	ROM monitor current address.
$0100	NMI address.
$01C0	IRQ address.
$0200	Cursor position for BASIC output is $D300 +($0200). Default (bottom left) is $65.
$0203	LOAD flag ($80=load from tape).
$0205	SAVE flag (0=not in save mode). In BASIC, POKE 517,0 to turn off save mode
$0212	BASIC <Control>C flag (non-zero=ignore <Control>C). Reset by RUN.
$023E,$023F	Address of BASIC USR() function.
$A274	BASIC warm start.
$BD11	BASIC cold start.
$BF2D	Send character in A to terminal screen. Handles CR, LF, etc.
$FCB1	Send character in A to ACIA.
$FD00	Get key from keyboard and return in A.
$FE00	ROM monitor entry point.
$FE80	Get character from ACIA and return in A.
$FEED	Calls $FD00.
$FF00	Reset address.
$FF69	Output character to screen via $BF2D, and if SAVE flag is non-zero, also to serial/tape.
$FFBA	Get key from keyboard, or if LOAD flag has high bit set, from serial/tape.
$FFEB	BASIC input routine. Via vector in $0218,9 calls $FFBA.
$FFEE	BASIC output routine. Via vector in $021A,B calls $FF69.
$FFFA,$FFFC	NMI vector.
$FFFC,$FFFD	Reset vector.
$FFFE,$FFFF	IRQ vector.

Microsoft BASIC

Commands: CONT, LIST, NEW, NULL, RUN

Statements: CLEAR, DATA, DEF, DIM, END, FN, FOR, GOSUB, GOTO, IF, INPUT, LET, LOAD, NEXT, NOT, NULL, ON, OR, POKE, PRINT, READ, REM, RESTORE, RETURN, SAVE, STEP, STOP, THEN, TO, WAIT, ?

Functions: ABS(), ASC(), ATN(), CHR$(), COS(), EXP(), FRE(), INT(), LEFT$(), LEN(), LOG(), MID$(), PEEK(), POS(), RIGHT$(), RND(), SGN(), SIN(), SPC(), SQR(), STR$(), TAB(), TAN(), USR(), VAL()

Operators: +, -, *, /, ^, NOT, AND, OR, =, <, >, <>, >=, <=

Editing:

<Shift>N ^ character	<Shift>+O	Erase last character
<Shift>+P	Erase current line	<Control>+C	Interrupt running program or LIST command
<Control>+O	Suspend output until typed again

Boot Prompt

D/C/W/M ?_
 | | | |
 | | | └─→ ROM Monitor
 | | └───→ Warm start (does not clear any BASIC program)
 | └─────→ Cold start (clears any BASIC program)
└──────→ Disk boot (requires disk controller)

Miscellaneous

Default video is 25 chars x 25 lines. Power on with BREAK key down to get 32 chars x 28 lines. BASIC always uses 24x24.

Serial Port protocol: 9600 bps, 8N1, no flow control or hardware handshaking. For BASIC, use 50ms char delay, 200ms line delay.

Sample Linux commands to initialize serial port and send file:
    stty -hup -clocal raw 9600 </dev/ttyUSB0
    ascii-xfr -s -l 200 -c 50 program.bas >/dev/ttyUSB0

        25x25 Video Mode
Hex Dec Hex Dec
D085 53381 □□□□□□□□□□□□□□□□□□□□□□□□□ 53405 D09D
D0A5 53413 □□□□□□□□□□□□□□□□□□□□□□□□□ 53437 D0BD
D0C5 53445 □□□□□□□□□□□□□□□□□□□□□□□□□ 53469 D0DD
D0E5 53477 □□□□□□□□□□□□□□□□□□□□□□□□□ 53501 D0FD
D105 53505 □□□□□□□□□□□□□□□□□□□□□□□□□ 53533 D11D
D125 53541 □□□□□□□□□□□□□□□□□□□□□□□□□ 53565 D13D
D145 53573 □□□□□□□□□□□□□□□□□□□□□□□□□ 53597 D15D
D165 53605 □□□□□□□□□□□□□□□□□□□□□□□□□ 53629 D17D
D185 53637 □□□□□□□□□□□□□□□□□□□□□□□□□ 53661 D19D
D1A5 53669 □□□□□□□□□□□□□□□□□□□□□□□□□ 53693 D1BD
D1C5 53701 □□□□□□□□□□□□□□□□□□□□□□□□□ 53725 D1DD
D1E5 53733 □□□□□□□□□□□□□□□□□□□□□□□□□ 53757 D1FD
D205 53765 □□□□□□□□□□□□□□□□□□□□□□□□□ 53789 D21D
D225 53797 □□□□□□□□□□□□□□□□□□□□□□□□□ 53821 D23D
D245 53829 □□□□□□□□□□□□□□□□□□□□□□□□□ 53853 D25D
D265 53861 □□□□□□□□□□□□□□□□□□□□□□□□□ 53885 D27D
D285 53893 □□□□□□□□□□□□□□□□□□□□□□□□□ 53917 D29D
D2A5 53925 □□□□□□□□□□□□□□□□□□□□□□□□□ 53949 D2BD
D2C5 53957 □□□□□□□□□□□□□□□□□□□□□□□□□ 53981 D2DD
D2E5 53989 □□□□□□□□□□□□□□□□□□□□□□□□□ 54014 D2FD
D305 54021 □□□□□□□□□□□□□□□□□□□□□□□□□ 54045 D31D
D325 54053 □□□□□□□□□□□□□□□□□□□□□□□□□ 54077 D33D
D345 54085 □□□□□□□□□□□□□□□□□□□□□□□□□ 54109 D35D
D365 54117 □□□□□□□□□□□□□□□□□□□□□□□□□ 54141 D37D
D385 54149 □□□□□□□□□□□□□□□□□□□□□□□□□ 54172 D39D

        32x28 Video Mode
Hex Dec Hex Dec
D080 53376 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53407 D09F
D0A0 53408 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53439 D0BF
D0C0 53440 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53471 D0DF
D0E0 53472 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53503 D0FF
D100 53504 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53535 D11F
D120 53536 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53567 D13F
D140 53568 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53599 D15F
D160 53600 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53631 D17F
D180 53632 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53663 D19F
D1A0 53664 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53695 D1BF
D1C0 53696 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53727 D1DF
D1E0 53728 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53759 D1FF
D200 53760 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53791 D21F
D220 53792 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53823 D23F
D240 53824 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53855 D25F
D260 53856 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53887 D27F
D280 53888 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53919 D29F
D2A0 53920 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53951 D2BF
D2C0 53952 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 53983 D2DF
D2E0 53984 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 54016 D2FF
D300 54016 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 54047 D31F
D320 54048 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 54079 D33F
D340 54080 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 54111 D35F
D360 54112 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 54143 D37F
D380 54144 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 54175 D39F
D3A0 54176 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 54207 D3BF
D3C0 54208 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 54239 D3DF
D3E0 54240 □□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□□ 54271 D3FF