65816 Microprocessor Quick Reference
Jeff Tranter <tranter@pobox.com>
Updated: 03-Jul-2012
Registers:

23	22	21	20	19	18	17	16	15	14	13	12	11	10	9	8	7	6	5	4	3	2	1	0
Data Bank Register (DBR)								Accumulator (B)								Accumulator (A)
								X Index Register (X)
								Y Index Register (Y)
0	0	0	0	0	0	0	0	Direct Page Register (D)
0	0	0	0	0	0	0	0	Stack Pointer (S)
Program Bank Register (PBR)								Program Counter (PC)
								Processor Status Register (P)															E
																N	V	M	X	D	I	Z	C

Notes:
1. Accumulator is 16-bit (C) when M=0, 8-bit (A and B) when M=1.
2. Index registers are 16-bit when X=0, 8-bit when X=1.

Processor Status Register:
N - Negative (1=negative)	V - Overflow (1=overflow)
M - Memory/Accumulator Select (1=8-bit, 0=16-bit)	X - Index Register Select (1=8-bit, 0=16-bit)
D - Decimal Mode (1=decimal, 0=binary)	I - IRQ Disable (1=disabled)
Z - Zero (1=zero result)	C - Carry (1=carry)
E - Emulation (0=native mode)

Switching Modes:

Go to native mode:	Go to emulation mode:
CLC	SEC
XCE	XCE

Select 16-bit memory and 16-bit index registers:	Select 8-bit memory and 8-bit index registers:
REP #%00110000	SEP #%00110000
Select 16-bit memory and 8-bit index registers:	Select 8-bit memory and 16-bit registers:
REP #%00100000	SEP #%00100000
SEP #%00010000	REP #%00010000

Emulation Mode Features:

1. Emulation mode is default on power up/reset.
2. Separate 8-bit accumulators (A and B).
3. 8-bit index registers (X and Y).
4. Stack is limited to page 1.
5. Direct page indexing wraps.
6. B flag in P reflects BRK status (instead of X).
7. Uses 6502 interrupt vectors.

New Addressing Modes:

Addressing Mode	Example
Program Counter Relative Long	BRL JMPLABEL
Stack Relative	LDA 3,S
Stack Relative Indirect Indexed with Y	LDA (5,S),Y
Block Move	MVP 0,0
Absolute Long	LDA $02F000
Absolute Long Indexed with X	LDA $12D080, X
Absolute Indirect Long	JMP [$2000]
Direct Page Indirect Long	LDA [$55]
Direct Page Indirect Long Indexed with Y	LDA [$55], Y

New Instructions:

BRL	Branch always long	REP	Reset status bits
COP	Co-processor empowerment	RTL	Return from subroutine long
JML	Jump long	SEP	Set status bits
JSL	Jump to subroutine long	STP	Stop the processor
MVN	Block move negative	TCD	Transfer 16-bit accumulator to direct page register
MVP	Block move positive	TCS	Transfer accumulator to stack pointer
PEA	Push effective absolute address onto stack	TDC	Transfer direct page register to 16-bit accumulator
PEI	Push effective indirect address onto stack	TSC	Transfer stack pointer to 16-bit accumulator
PER	Push effective PC relative address onto stack	TXY	Transfer index registers X to Y
PHB	Push data bank register onto stack	TYX	Transfer index registers Y to X
PHD	Push direct page register onto stack	WAI	Wait for interrupt
PHK	Push program bank register onto stack	WDM	Reserved for future two-byte opcodes
PLB	Pull data bank register from stack	XBA	Exchange the B and A accumulators
PLD	Pull direct page register from stack	XCE	Exchange carry and emulation bits

Interrupt Vector Locations:

Vector	Emulation Mode	Native Mode
IRQ	$FFFE, $FFFF	$FFEE, $FFEF
RESET	$FFFC, $FFFD	-
NMI	$FFFA, $FFFB	$FFEA, $FFEB
ABORT	$FFF8, $FFF9	$FFE8, $FFE9
BRK	-	$FFE6, $FFE7
COP	$FFF4, $FFF5	$FFE4, $FFE5

Note: All locations are in bank zero.