KIM-1 Quick Reference
For the MOS Technology KIM-1 Microcomputer Module
Jeff Tranter <tranter@pobox.com>

NMI Initialization for Single Step and Stop:

17FA 00	17FB 1C

IRQ Initialization for BRK:

17FE 00	17FF 1C

Machine Context (saved/restored by ST/GO):

00EF PC low	00F0 PC high
00F1 Status Register (flags)	00F2 Stack Pointer
00F3 A	00F4 Y
00F5 X

Breakpoints: Write BRK instruction ($00) at desired address.
ST button: Pressing will invoke NMI interrupt.
Single Step: Set SST switch to on, press GO button to step one instruction.

Cassette Load and Save

Successful save or load indicated on display with 0000 XX, bad load with FFFF XX.
12 Volt power source is required when reading tapes.

To save:
1. Store $00 in $00F1 (to ensure CPU is in binary mode).
2. Save start address (low/high) in $17F5, $17F6.
3. Save end address+1 (low/high) in $17F7, $17F8.
4. Write tape ID ($01-$FE) in $17F9.
5. Start tape in record mode.
6. Run address $1800 (DUMPT) to save.

To load:
1. Store $00 in $00F1 (to ensure CPU is in binary mode).
2. Write tape ID ($01-$FE, $00 loads any ID, $FF loads using start address values) to $17F9.
3. Run address $1873 (LOADT) to load.

Teleprinter Commands

Serial port settings 9600 bps (or less) 8N2. Press <Rubout> or <Delete> after Reset to initialize serial bit rate.

<hex address> <space>	Show data at address
<hex data> .	Write to current address
<Return>	Advance to next address
<Line Feed>	Move to previous address
<Rubout>	Terminate memory edit
L	Load program from paper tape
Q	Save memory to paper tape (saves from current address to $17F7, $17F8)
G	Go from current address

Memory Map
Range	Comments
$0000 - $00FF	RAM - page zero ($00EF - $00FF are reserved)
$0100 - $01FF	RAM - stack
$0200 - $03FF	RAM - user programs
$1700 / $1740	I/O Register A
$1701 / $1741	Direction Register A
$1702 / $1742	I/O Register B
$1703 / $1743	Direction Register B
$1704 / $1744	Write: Timer, 1 usec, no interrupt
$1705 / $1745	Write: Timer, 8 usec, no interrupt
$1706 / $1746	Write: Timer, 64 usec, no interrupt. Read: timer count, disable interrupt.
$1707 / $1747	Write: Timer, 1024 usec, no interrupt. Read: timer status, Bit 7 = 1 on timeout.
$170C / $174C	Write: Timer, 1 usec, interrupt
$170D / $174D	Write: Timer, 8 usec, interrupt
$170E / $174E	Write: Timer, 64 usec, interrupt. Read: timer count, enable interrupt.
$170F / $174F	Write: Timer, 1024 usec, interrupt
$1780 - $17E6	Application RAM
$17E7 - $17FF	KIM RAM
$1800 - $1FFF	KIM ROM (2K)
$FFF8 - $FFFF	Reset, NMI, IRQ, and BRK vectors (in ROM).

Useful ROM Routines
Name	Address	Description
DUMPT	$1800	Write (Dump) to audio tape.
LOADT	$1873	Read (Load) from audio tape.
ONE	$199E	Send 3700 Hz tone to tape.
ZRO	$19C4	Send 200 Hz tone to tape.
PLLCAL	$1A6B	Send 300 Hz PLL reference tone to tape.
AK	$1EFE	Check for key depressed. A non-zero: no key down. A equal 0, key down.
SCAND	$1F19	Display address and contents.
SCANDS	$1F1F	Output six hex characters on display. Stored in $00F9, $00FA, $00FB.
KEYIN	$1F40	Open up keyboard channel. Call before using GETKEY (or call SCANDS).
INCPT	$1F63	Increment display address.
GETKEY	$1F6A	Return key from keyboard. Value 0-F, 10(AD), 11(DA), 12(+), 13(GO), 14(PC), 15 (no keypress).
TABLE	$1FE7	Table of 7-segment patterns.
	$1C2A	Set TTY baud rate.
PRTPNT	$1E1E	Prints contents of $00FB, $00FA on TTY.
CRLF	$1E2F	Send CRLF to TTY.
PRTBYT	$1E3B	Prints A as two hex characters on TTY.
GETCH	$1E5A	Get one ASCII character from TTY and return in A.
OUTSP	$1E9E	Print space on TTY.
OUTCH	$1EA0	Print ASCII character in A on TTY.
GETBYT	$1F9D	Get two hex characters from TTY and return them packed in A.
SAVE	$1C00	Normal interrupt entry point.
RST	$1C22	Reset return to monitor.
START	$1C4F	Return to monitor entry.

Connector Pinouts
Connector B (upper) Expansion Connector. Pins 1-22 ontop, A-Z on bottom.
Pin	Signal	Pin	Signal
1	SYNC	A	AB0
2	RDY	B	AB2
3	Ø1	C	AB2
4	IRQ	D	AB3
5	RO	E	AB4
6	NMI	F	AB5
7	RST	H	AB6
8	DB7	J	AB7
9	DB6	K	AB8
10	DB5	L	AB9
11	DB4	M	AB10
12	DB3	N	AB11
13	DB2	P	AB12
14	DB1	R	AB13
15	DB0	S	AB14
16	K6	T	AB15
17	SST OUT	U	Ø2
18		V	R/W
19		W	R/W
20		X	PLL TEST
21	VCC +5V	Y	Ø2
22	VSS GND	Z	RAM/R/W

Connector A (lower) Application Connector. Pins 1-22 on top, A-Z on bottom.
Pin	Signal	Pin	Signal
1	VSS GND	A	VCC +5V
2	PA3	B	K0
3	PA2	C	K1
4	PA1	D	K2
5	PA4	E	K3
6	PA5	F	K4
7	PA6	H	K5
8	PA7	J	K7
9	PB0	K	DECODE ENAB
10	PB1	L	AUDIO IN
11	PB2	M	AUDIO OUT LO
12	PB3	N	+12V
13	PB4	P	AUDIO OUT HI
14	PA0	R	TTY KYBD RTRN(+)
15	PB7	S	TTY PTR RTRN(+)
16	PB5	T	TTY KYBD
17	KB Row 0	U	TTY PTR
18	KB Col F	V	KB Row 3
19	KB Col B	W	KB Col G
20	KB Col E	X	KB Row 2
21	KB Col A	Y	KNB Col C
22	KB Col D	Z	KB Row 1