65C02 Microprocessor Quick Reference
Jeff Tranter <tranter@pobox.com>
Updated: 10-Jul-2012

This sheet summarizes the software extensions and differences for the 65C02 processor over the NMOS 6502.

New Addressing Modes:

Indirect Zero Page	e.g. LDA ($12)
Absolute Indexed Indirect	e.g. JMP ($1234,X)

New Instructions:

BRA nn	Branch Always
PHX	Push X
PHY	Push Y
PLX	Pull X
PLY	Pull Y
STZ nn	Store Zero
STZ nn,X	Store Zero
STZ nnnn	Store Zero
STZ nnnn,X	Store Zero
TRB nn	Test and Reset Bit
TRB nnnn	Test and Reset Bit
TSB nn	Test and Set Bit
TSB nnnn	Test and Set Bit

Instructions With New Addressing Modes:

ADC (nn)	EOR (nn)
AND (nn)	INC A
BIT #nn	JMP (nnnn,X)
BIT nn,X	LDA (nn)
BIT nnnn,X	ORA (nn)
CMP (nn)	SBC (nn)
DEC A	STA (nn)

Enhancements:

Invalid op codes are executed as NOPs.
JMP (nnFF) correctly increments page address.
Decimal flag is cleared on reset and interrupt.
N, V, and Z flags are valid in decimal mode.

Rockwell and Western Design Center 65C02-Specific Instructions:

BBR	-	Branch on Bit Reset
BBS	-	Branch on Bit Set
RMB	-	Reset Memory Bit
SMB	-	Set Memory Bit

Western Design Center 65C02-Specific Instructions:

STP	-	Stop Processor
WAI	-	Wait For Interrupt